Internetworking

Network Segmentation and Connections

Accomplished using routers, switches, bridges

Routers – Layer 3

Break up broadcast domains

Break up collision domains

Advantages

Don’t forward broadcasts by default

Filter network based layer three (Network layer) information, i.e. IP addresses

Memorize

Routers, by default, do not forward broadcasts/multicast packets

Routers use logical address in network layer header to determine next hop router

Routers use access lists created by administrator to control security

Routers provide layer 2 bridging functions if necessary

Can simultaneously Route through same interfaces

Provide connections between virtual LANs

Can provide quality of service QOS for specific types of network traffic

Switches – Layer 2

Break up collision domains

Each port creates collision domain

Not used to create internetworks

Employed to add functionality to internetwork LAN

Make LAN work better-optimize performance

Provide more bandwidth

Do not forward packets to other networks

Only switch frames from one port to another within switched network

Each network segment on switch must have same type of devices attached

Cannot mix Ethernet with Token Ring

Bridge – Layer 2

Reduces collisions within broadcast domain

Increases number of collision domains

Thereby providing more bandwidth

Bridges and Switches

Read each frame as they pass through network

Layer 2 device puts source hardware address in filter table

Keeps track which port frame was received

Allows device to determine location of specific sending device

Only forwards frames to segment where destination hardware address is located

Will block forwarding if device is on same segment

WILL forward frame to correct segment - TRANSPARENT BRIDGING

If switch receives frame with unknown destination hardware address

(Not recorded in filter table)

Forwards frames to all connected segments

Could be problematic because broadcast storm is created

Only solution to stop broadcast storms is use a router

If destination found switch updates its filter table

This is why Switch/Bridge is same broadcast domain

Switches advantage over bridges

Break up collision domains

Switches over hubs

Each device plugged into switch can transmit simultaneously

Broadcast Domain

Set of all devices on network segment that hear all broadcasts

Collision Domain

Device sends packets on network segment

Forces all other devices to pay attention to it

Reference Model Layered Approach

Blueprint of how communications should take place

Divides processes into layers

Advantages

Allows multiple vendor development through standardization of network components

Allows various types of network hardware/software to communicate

Prevents changes in one layer from affecting other layers

OSI Reference Model

Top Three Layers define how applications within end stations communicate

1. Application - provides user interface

2. Presentation -presents data, handles processing such as encryption

3. Session - keeps different applications data separate

Bottom four layers define how data transmitted end to end

Determine how to rebuild DataStream from transmitting host

4. Transport -provides reliable/unreliable delivery

Segments

Performs error correction before retransmission

5. Network -provides logical addressing and path determination

Packets

6. Data Link -combine packets into bytes and bytes into frames

Frames

Provides access to media using MAC addresses

Performs error detection not correction

7. Physical - moves bits between devices

Specifies voltage, wire speed, and pin out of cables

Network devices operating at all seven layers include

Network management stations

Web and application servers

Gateways (not default gateways)

Network hosts

Application - file, print, message, database, application services

Presentation - data encryption, compression, translation

Session - dialog control

Transport - end to end connection

Network - routing

Data Link - framing

Physical - physical topology

Application Layer

Users actually communicate to the computer

Responsible for identifying/establishing availability of intended communication partner

Determines whether sufficient resources exist

Examples

WWW

E-mail

Electronic data interchange EDI

Special interest bulletin boards

Internet navigation utilities goggle

Presentation Layer

Presents data to application layer

Responsible for data translation/code formatting

Presentation layer standards for multimedia

Tiff, JPEG, MIDI etc.

Session Layer

Setting up, managing, tearing down sessions

Provides dialog control between devices

Coordinates communication between systems

Keeps different applications data separate

Offers

Simplex

Half duplex

Full duplex

Examples

Network File Systems

SQL

RPC

Transport Layer

Segments and reassembles data into DataStream

Provides end to end data transport services

Establishes logical connection between hosts and destination

Example

TCP

UDP

Flow Control

Prevents one side from overflowing buffers in receiving host

Segments delivered and acknowledged back to sender upon receipt

Non-acknowledged segments retransmitted

Segments sequenced into proper order upon arrival

Manageable dataflow prevents congestion, overloading, data loss

Connection Oriented Communication

Call setup involves three-way handshake

- Sender sends synchronization

- receiver sends synchronization

  - Sender/ receiver negotiate connection

  - Window size, etc.

- sender acknowledges receiver's synchronization

Connection is established

Flood Control done with windowing

Window is quantity of data segments (measured in bytes)

Transmitting machine allowed sending without receiving acknowledgment

Acknowledgments

Positive acknowledgment with retransmission

Network Layer - layer three

Manages device addressing

Tracks location of devices on networks

Determines best way to move data

Only care about where networks are located and how to reach them

Example

Packet received on router interface

Destination IP address checked

Destination network address looked up in routing table

Router determines exit interface

Packet framed and sent

Two types of packets

Data Packets-transport user data through internetwork

Utilizes routing protocols

Example: IP, IPX

Route Update Packets

Update neighboring routers about networks connected to routers

Common protocols-RIP EIGRP, OSPF

Network Addresses

Protocol specific network addresses maintained in routing table

Interface - exit interface packet takes for specific network

Metric - distance often measured in hop counts

Data Link Layer

Provides physical transmission of data

Handles error notification, network topology, flow control

Ensures messages delivered to proper device on LAN using hardware addresses

Translates messages from network layer in tidbits for physical layer

Responsible for unique identification of each device

Data Frame

Formats messages into pieces called data frames

Adds customized header containing hardware destination and source address

Two sub layers

1. Media Access Control MAC

Define how packets placed on media

First-come/first-served

Everyone shares same bandwidth

Physical addressing as well as local topologies

Line discipline, error notification, ordered delivery of frames, optional flow control

2. Logical Link Control LLC

Identifying network layer protocols encapsulate them

LLC header tells data Link layer what to do with packet

Example

Host receives a frame

Looks at LLC header and determines where packet is destined

Switches and Bridges at Data Link Layer

Hardware based bridging uses specialized hardware called

Application Specific Integrated Circuit ASIC

Run at gigabit speeds with low latency

Physical Layer

Sends and receives bits

Data Terminal Equipment DTE

Data Communication Equipment DCE

Hubs at Physical Layer

Hub is multiple port repeaters

Receives digital signal, reenergize, regenerate signal

Ethernet Networking

Contention media access method allows hosts to share network bandwidth

Carrier Sense Multiple Access with Collision Detection CSMA/CD

Readily scalable-easy to integrate new technologies

Only Bridges and routers prevent transmission from propagating through entire network

Bridge (( Switch

Bridge software

Switch hardware

CSMA/CD

- Check presence a digital signal on wire

- if clear proceed with transmission

- constantly monitor wire to ensure no other transmissions

- if transmission detected send out extended jam signal

- other stations use BackOff algorithms

Half and Full duplex Ethernet

Half Duplex

Single wire with digital signal running in both directions

If hub is attached to switch must operate in half duplex mode

End stations must detect collisions

Full Duplex

Two pairs of wires

Uses point-to-point connection between transmitter and receiver

Prior bandwidth no collisions

Used when

Connection between switch and host

Connection between switch and switch

Connection between host and host using crossover cable

Ethernet Addressing

Uses Media Access Control MAC address burned into Network Interface Card NIC

48 bit-six byte address written in hexadecimal format

24 bits organizationally assigned unique identifier

24 bits vendor assigned

High Order Bit is individual group I/G bit

Zero means address is Mac address

One means broadcast/multicast address

Ethernet Frames

Provides error detection from cyclic redundancy check CRC

Preamble

Alternating1, 0 patterns provides 5MHz clock at beginning of each packet

Allows synchronization of incoming bit stream

Start Frame Delimiter

Preamble is seven octets – SFD is one octet

Destination Address

48 bit value using least significant bit first

Allows receiving stations to determine whether packet is for them

Attenuation

Defined as loss of signal strength as it travels length of cable

Measured in decibels

Crosstalk

Unwanted signal interference from adjacent pairs in cable

Ethernet Cabling

Straight through cable

Host to switch or hub

Router to switch or hub

Four wires used in straight through cable

Crossover cable

Switch to switch

Hub to hub

Host to host

Hub to switch

Router direct to switch

Pins reversed

Rolled cable

Connects host to router console serial com port

10Base2

10 megabits per second-185 m in length

Thinnest

10Base5

10 megabits per second, 500 m in length

Thick net

Wireless Networking

Spread Spectrum wireless LANs

Data Encapsulation

Transmitted data wrapped with protocol information at each layer of OSI model

Protocol information usually attached as header

Each layer communicates only with other peer layers

Encapsulated into Protocol Data Units

Example Process

DataStream handed to Transport layer which setup virtual circuit

Sends synchronization packet

DataStream broken into smaller pieces and transport layer header created

Data now called a segment

Segments sequenced

Segment handed to network layer for addressing routing

Logical addressing (IP) Routes segment to correct network

Network layer adds header and hands to transport layer

Now called a packet or datagram

Data Link layer takes packets from network layer and places them on network medium

Encapsulate each packet in a frame

Frame header carries hardware address of source and destination hosts

Physical layer places ones and zeros on network

Creates CRC

Cisco Three-Layer Hierarchical Model

Core Layer

Backbone

Distribution Layer

Routing

Access Layer

Switching

Core Layer

Top hierarchy responsible for transporting large amounts of traffic reliably/quickly

( Switch traffic as fast as possible

Failure at core affects all users ( full tolerance is initiated

Essential Goals

Do not slowdown traffic (includes no access lists, filtering, WANs

Don’t support workgroup access

Avoid expanding core IE adding routers

Designed for high reliability

Designed for speed

Select routing for lower convergence times

Distribution Layer

Workgroup layer

Provide routing, filtering WAN access

Determine how packets access core

Determine quickest network service

Goals and tasks

Routing

Implementation of tools, access lists, packet Filtering, Queuing

Implementation of security and network policies

Address translation and firewalls

Redistribution between routing protocols and static routing

Routing between LANs

Definitions of broadcast/multicast domains

Access Layer

Controls user/workgroup access to internet work

Also called desktop layer

Resources most users need available locally

Goals and functions

Access control and policies

Creation of separate collision domains (segmentation)

Workgroup connectivity to distribution layer

Internet Protocols

Transmission Control Protocol/Internet Protocol (TCP/IP)

Protocol suite created by Department of Defense (DOD & DARPA)

Preserve data integrity, maintain communications in event of catastrophic war

If implemented correctly TCP/IP network dependable and resilient

DOD TCP/IP Model

Condensed version of OSI model with four layers

- Process/Application layer

( OSI Application/Presentation Session layers

Node to node application communication

Controls user interface specifications

Example: telnet FTP SMTP NFS SNMP

- Host to Host layer

( OSI Transport layer

Defines protocols for setting level of transmission service

Reliable end to end communication

Ensures error free delivery of data

Packet sequencing and data integrity

Examples: TCP UDP

- Internet layer

( OSI Network layer

Designates protocols for logical transmission over entire network

Handles addressing of hosts using IP address

Handles routing of packets among multiple networks

Examples: IP ARP

- Network Access layer

( OSI Datalink/Physical layers

Data exchange between host and network

Hardware addressing

Physical transmission of data protocols

Examples: Ethernet Token ring Fast Ethernet

Applications

Telnet

Terminal emulation

Allows user on remote client machine (Telnet client with installed software)

To access resources of another machine (Telnet server)

Projection is actually software image-virtual terminal

Text mode communication

File Transfer Protocol (FTP)

Not just a protocol but also program operating as a protocol

Used by applications as a protocol

Used by users as a program

Allows access to both directories and files

Teams up with Telnet to transparently laud you into FTP server

Requires authentication

No limit on file size

E-mail restricted to 5MB

Quicker than e-mail

Network File System (NFS)

Specializes in file sharing

Allows different types of file systems to interoperate

Server transparently reserves portion of RAM to store file

Access by any other differing operating system

Simple Mail Transfer Protocol (SMTP)

Spooled or queued Mail delivery

Spooled to disk

Sends mail

POP3

Receives Mail

X Window

Client/server operations

Defines protocol for applications based on GUI

Simple Network Management Protocol (SNMP)

Collects and manipulates valuable network information

Gathers data by polling devices on network at fixed/random intervals

If all is well SNMP receives baseline report

Domain Named Service (DNS)

Resolves host names specifically Internet names

Fully Qualified Domain Name (FQDN)

Dynamic Host Configuration Protocol (DHCP)/BootP (Bootstrap Protocol)

Gives IP addresses to hosts

BootP differs in that hardware address must be manually entered in BootP table

DHCP servers provide

IP address

Subnet mask

Domain name

Default gateway (routers)

DNS

Host to Host Layer Protocols

Transmission Control Protocol the TCP

User Datagram Protocol UDP

TCP

Full duplex, connection oriented, reliable, accurate protocol

Costly in terms of overhead

Added reliability often unnecessary with today's more liable networks

Takes large blocks of information from an application and breaks them into segments

Numbers and sequences each segment so destination TCP can reorder for intended application

After sending waits for acknowledgment from end TCP's virtual circuit

Resends segments not acknowledged

Virtual Circuit-connection oriented

Sender TCP contacts destination TCP to establish connection

Agree on amount of information to be sent prior to acknowledgment

UDP

Connectionless

Thin protocol	= low overhead

Can be used when reliability handled at process/application layer

NFS handles its own reliability

Does not sequence segments or care about arrival order

Does not require acknowledgments

Port Numbers

TCP and UDP use Port numbers to communicate with the upper layers

Necessary to keep track of data destinations of network traffic

Originating source Port numbers dynamically assigned by source host

= number starting at 1024

Below 1023 defined by RFC 3232 and are well-known Port numbers

Virtual Circuits

Don’t use an application with well-known Port number

Randomly assigned from a specific range

Port numbers identify source and destination application/process in TCP segment

Well Known Port numbers

FTP 21

Telnet 23

Doom 666

DNS 53

T. FTP 69

POP3 110

News 119

Internet Layer Protocols

Two main reasons for existence

- Routing

- provide single network interface to upper layers

Without this applications would need hooks into network access protocol

Would lead to different versions for each application

One for Ethernet

One for Token Ring

It’s better

Protocols

IP

Internet Control Message Protocol ICMP

Address Resolution Protocol ARP

Reverse Address Resolution Protocol RARP

Internet Protocol

Essentially the Internet layer - all other protocols exist to support IP

Aware of all interconnected networks

All machines on network have software/logical address called IP address

Example

IP looks at each packet’s address

Uses routing table to decide where packet sent next choosing best path

- Which network is it on -Logical Address (street address)

- what is IP of this network –

Receives segments from host to host layer and fragments them into datagram’s (packets)

Reassembles at other end

Each router receives datagram and makes routing decisions based on destination IP

Internet Control Message Protocol ICMP

Works at network layer-used by IP from many services

Management protocol and messaging service provider for IP

Messages carried as IP datagrams

Example

Router advertisements announced over network

Report IP addresses for routers network interfaces

Hosts listen and update their router tables

Common Events

Destination Unreachable-router can’t send IP datagram any further

Sends a message back to origins

Buffer Full

Router buffer full

Sends message until congestion abates

Hops

Each IP datagram allotted certain number of hops

If it exceeds hop count sends message noting failure

Ping-Packet Internet Groper

Uses ICMP to echo messages checking physical/logical connectivity

Traceroute

Using ICMP timeouts discovers packets path during traversal of network

Address Resolution Protocol

Finds hardware address of host from one IP address

Translates software (IP) address into hardware address

Example

IP has datagram to send

Informs network access protocol (Ethernet) of destination hardware's address

If IP doesn't find host hardware address uses ARP to determine

ARP interrogates local networks by sending out broadcasts

Asks for machine with specified IP address to reply with hardware address

Reverse Address Resolution Protocol RARP

Diskless IP machine often doesn't know its IP address

It knows its MAC address

RARP discovers identity of IP address for diskless machines

Binary to Decimal conversion

IP Addressing

Numeric identifier assigned to each machine on IP network

Designates specific location of device on network

Software address (not the Mac address located on Network Interface Card NIC)

Network Address-designation used in routing to send packets

Broadcasts Address-address used to send information to all nodes on network

Hierarchical IP Addressing Scheme

IP address is 32 bits of information

Divided into four section referred to as octets (bytes)

Hierarchical as opposed to flat address

Makes routing easier

Depicted in three methods

- Dotted decimal

- binary

- hexadecimal (Windows Registry uses hex)

Network Addressing

Uniquely identifies each address

Every machine on same network shares network address

Node Address

Assigned to and uniquely identifies each machine on network

Classes

To ensure efficient routing-define mandate for leading bits section

Class A - always begins with a zero

Quite possible router could speed packet on its way after reading first bit

Class A

Always begins with a zero

Addresses between zero and 127

00000000 – 01111111

Octets between zero and 127

Example

Network.node.node.node

All zeros cannot be used-default route

127 reserved for diagnostics

1-126 are usable

Class B

First bit is 1 second bit is zero – 10

10000000 = 128

10111111 = 191

Example

Network.network.node.node

10 beginning leaves 14 bits to manipulate 2 **14

( 65,534

Class C

First two bits of octets are 11 third bit is 0

11000000 = 192

11011111 = 223

Example

network.network.network.node

Begins with 110

24 bits minus 3 bits ( 2**21 or 2,097,152

Class D & E

224 - 255 reserved for class D & E

Class D is multicast 224-239

Class E is scientific 240-255

Special Purpose Addresses

All zeros-this network or segment

All ones-all networks

127.0.0.1-loopback test

Node address all zeros-network address any host specified network

Node address all ones-	all nodes on specified network

IP address all zeros-Cisco routers designate default route

IP address all ones-broadcast all nodes

Private IP Addresses

Used on private network but not routable through Internet

Allow creation of well needed security

Conveniently saves valuable IP space

Network Address Translation NAT

Takes Private IP address and converts it for use on Internet

Broadcast Addresses

Layer 2 broadcasts-sent to all nodes on LAN

Hardware broadcast

Do not leave LAN boundary unless they become unicast

Hardware address is six bytes

Broadcasts (layer three) sent to all nodes on network

Example: ARP request

Host’s IP address of destination needs physical address

Unicast-sent to single destination host

Broadcast that has actual destination IP address

Typically sent to DHCP servers

Example

Host LAN sends out ff.ff.ff.ff.ff.ff destination broadcast for DHCP server

Router sees this as broadcast meant for DHCP server

Forwards request to IP address of DHCP server on another LAN

Multicast-sent from single source to many devices on different networks

Allows point to multipoint communication

Enables multiple recipients to receive messages

Without flooding messages to entire broadcast domain

Sends messages to IP multicast group addresses

Hosts must subscribe to group address

Network Address Translation

Private IP addresses require translation to global outside address using NAT

Necessary to conserve global address space however increases network security

Hides internal IP addresses from external network

Static NAT

Allows one to one mapping between local and global addresses

Requires one real Internet IP for every host on network

Dynamic NAT

Maps unregistered IP addresses to registered IP addresses

Uses pool of registered IP addresses

Not necessary to static reconfigure router or mapping

Must have enough real IP addresses for everyone

Overloading-most important

Dynamically maps multiple unregistered IP addresses to single registered IP address

(Many to one) by using different ports

Known as Port Address Translation (PAT)